## Slide 1
MINI PROJECT 2B
Team Members:
1 Choudhry Abdul Rehman Mohd Asim
2 Sadriwala Mohammed Firoz
3 Shaikh Adyan Ataullah
4 Pathan Mugaira Zakeer
Guide: PROF. SHIBURAJ PAPPU
Emotion Lamp — Converts Ambient Sound Patterns to Light Moods

## Slide 2: Problem Statement
In modern indoor environments such as homes, offices, and study spaces, ambient emotional conditions often go unnoticed despite having a significant impact on human comfort and productivity. Existing sound-reactive lighting systems primarily focus on detecting music beats or volume levels, which limits their applicability and expressiveness. There is a need for an intelligent yet low-cost system that can interpret environmental sound patterns, such as voice tone, amplitude, silence, and sudden noise, and convert them into meaningful visual feedback through lighting.

## Slide 3: ABSTRACT
Emotion Lamp is a simple IoT project that changes light color and intensity based on surrounding sound. It uses a microphone to measure sound volume and frequency patterns and maps them to different light moods in real time. The project focuses on visualizing the overall sound environment of a room rather than detecting individual emotions, demonstrating basic signal processing and embedded system control.

## Slide 4: TABLE OF CONTENTS
Introduction
Problem Statement
Literature Review
Requirement Analysis and Feasibility Study
Proposed System
Objectives of Proposed Work
Comparative Analysis
Conclusion
References

## Slide 5: INTRODUCTION
Context / Need
Indoor environments continuously reflect human activity and emotional states through ambient sounds such as conversations, silence, and sudden noise. Existing sound-reactive lighting systems mainly focus on music beat or volume detection, limiting their usefulness beyond entertainment. There is a need for an intelligent, low-cost system that interprets environmental sound patterns to provide meaningful and intuitive visual feedback.
Scope of the Project
This project analyzes ambient sound characteristics such as voice tone, amplitude variations, silence, and noise peaks, and maps them to corresponding light moods using RGB LEDs. The system operates in real time using embedded hardware and is suitable for indoor environments. The scope can be extended to environment classification and data logging for smart spaces.

## Slide 6: Requirement Analysis & Feasibility
Hardware Requirements
ESP32 WROOM32 Devkit1INMP441 MEMS Omnidirectional Microphone Module
WS28121B LED
Breadboard
470uf Capacitor
100nf capacitor
SN74HCT125N Buffer
68 Ohm resistor
Software Requirements
Arduino IDE / ESP-IDF
Signal processing algorithms
LED control libraries

## Slide 7: LITERATURE REVIEW
Existing Systems / Studies
Several studies and systems have explored sound-responsive lighting and emotion-aware environments. Traditional sound-reactive LED systems respond to changes in sound amplitude, while music beat detection systems synchronize lighting effects with musical rhythm using frequency analysis techniques. Some advanced studies focus on audio-based emotion detection using speech features and machine learning models to classify emotional states.
Limitations of Existing Systems
Most existing systems are limited to entertainment applications and depend heavily on music input. They fail to interpret emotional or contextual information from everyday environmental sounds. Machine learning-based emotion detection systems require high computational resources, large datasets, and expensive hardware, making them unsuitable for low-cost, real-time embedded applications.
Proposed System – Improvement and Differentiation
The proposed Emotion Lamp differs by focusing on environmental sound patterns rather than music beats or complex emotion classification. It analyzes voice tone characteristics, amplitude variations, silence, and sudden noise peaks to infer the emotional state of an environment. The system provides real-time visual feedback using low-cost hardware, making it affordable, scalable, and suitable for everyday indoor spaces.

## Slide 8: Comparative Table
Paper / System | Year | Method Used | Limitation / Gap Identified
Audio-Based Emotion Detection | 2021 | Machine learning on speech features | High computational cost, expensive hardware
Proposed Emotion Lamp | 2026 | Ambient Voice Tone + amplitude pattern analysis | Focused on basic affective states (extendable)

## Slide 9: Objectives of the Proposed Work
Project Objectives, Goals of the Proposed System, Intended Outcomes
To analyze environmental sound patterns instead of music beats
To map sound characteristics to intuitive light moods
To design a low-cost and real-time affective sensing system
To enhance ambient awareness through visual feedback
To optionally classify environments such as office, cafeteria, or study room

## Slide 10: Methodology of the Proposed Work
Approach & Implementation
The system adopts a real-time embedded approach where ambient sound is captured using a MEMS microphone and processed by an ESP32 microcontroller. Key sound features such as amplitude variation, voice tone tendency, silence duration, and sudden noise peaks are analyzed using threshold-based logic. Based on the detected pattern, the environment is classified into affective states, which are visualized using RGB LED light moods.
Project Workflow
Sound Capture → Signal Processing → Feature Analysis → Environment Classification → Light Mapping → RGB LED Output
System Architecture / Design Approach
The architecture consists of an Input Module (MEMS microphone), Processing Module (ESP32 for analysis and decision-making), and Output Module (WS2812 RGB LEDs for visualization). All modules operate in real time to provide continuous ambient feedback.

## Slide 11: CONCLUSION
The Emotion Lamp successfully demonstrates how environmental sound patterns can be transformed into meaningful visual representations. By focusing on affective cues rather than musical synchronization, the system offers a novel approach to ambient interaction. Its low cost, simplicity, and strong visual appeal make it suitable for academic projects, smart environments, and interactive installations. The project bridges the gap between technology and human perception, making emotions visible through light.

## Slide 12: REFERENCES
A. V. Oppenheim and R. W. Schafer, Discrete-Time Signal Processing, 3rd ed. Upper Saddle River, NJ, USA: Pearson Education, 2010.
L. R. Rabiner and R. W. Schafer, Theory and Applications of Digital Speech Processing. Upper Saddle River, NJ, USA: Pearson, 2011.
R. W. Picard, Affective Computing. Cambridge, MA, USA: MIT Press, 1997.
S. Scherer, G. Stratou, J. Gratch, and L.-P. Morency, “Automatic behavior descriptors for psychological disorder analysis,” IEEE Transactions on Affective Computing, vol. 4, no. 4, pp. 337–351, Oct.–Dec. 2013.
B. Schuller, S. Steidl, and A. Batliner, “The INTERSPEECH 2009 emotion challenge,” Proc. INTERSPEECH, Brighton, U.K., pp. 312–315, 2009.
Y. Kim and E. André, “Emotion recognition based on physiological changes in music listening,” IEEE Transactions on Pattern Analysis and Machine Intelligence, vol. 30, no. 12, pp. 2067–2083, Dec. 2008.
J. Deng, Z. Zhang, E. Marchi, and B. Schuller, “Sparse autoencoder-based feature transfer learning for speech emotion recognition,” Proc. IEEE ICASSP, pp. 4808–4812, 2014.

## Slide 13: ACKNOWLEDGEMENT
I am profoundly grateful to Prof. Shiburaj Pappu for his expert guidance and continuous encouragement. I would like to express deepest appreciation towards Dr. Varsha Shah, Principal RCOE, Mumbai and Prof. Mohd. Juned,HOD Department of Computer Engineering RCOE for their invaluable guidance. Finally, I must express my sincere heartfelt gratitude to all the staff members of the Computer Engineering Department.

## Slide 14: PAPER PUBLICATION